Worksheets from Orange County Technical Guidance Document (5-19-2011)

See TGD for instructions and/or examples related to these worksheets: www.ocwatersheds.com/WQMP.aspx

| Table 2.7: Infiltration BMP Feasibility Worksheet |
| --- |
|  | Infeasibility Criteria | Yes | No |
| 1 | Would Infiltration BMPs pose significant risk for groundwater related concerns? Refer to Appendix VII (Worksheet I) for guidance on groundwater-related infiltration feasibility criteria. |  |  |
| Provide basis: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |
| 2 | Would Infiltration BMPs pose significant risk of increasing risk of geotechnical hazards that cannot be mitigated to an acceptable level? (Yes if the answer to any of the following questions is yes, as established by a geotechnical expert): The BMP can only be located less than 50 feet away from slopes steeper than 15 percent The BMP can only be located less than eight feet from building foundations or an alternative setback. A study prepared by a geotechnical professional or an available watershed study substantiates that stormwater infiltration would potentially result in significantly increased risks of geotechnical hazards that cannot be mitigated to an acceptable level. |  |  |
| Provide basis: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |
| 3 | Would infiltration of the DCV from drainage area violate downstream water rights? |  |  |
| Provide basis: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |

| Table 2.7: Infiltration BMP Feasibility Worksheet (continued) |
| --- |
|  | Partial Infeasibility Criteria | Yes | No |
| 4 | Is proposed infiltration facility located on HSG D soils or the site geotechnical investigation identifies presence of soil characteristics which support categorization as D soils? |  |  |
| Provide basis: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |
| 5 | Is measured infiltration rate below proposed facility less than 0.3 inches per hour? This calculation shall be based on the methods described in Appendix VII. |  |  |
| Provide basis: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |
| 6 | Would reduction of over predeveloped conditions cause impairments to downstream beneficial uses, such as change of seasonality of ephemeral washes or increased discharge of contaminated groundwater to surface waters? |  |  |
| Provide citation to applicable study and summarize findings relative to the amount of infiltration that is permissible: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |
| 7 | Would an increase in infiltration over predeveloped conditions cause impairments to downstream beneficial uses, such as change of seasonality of ephemeral washes or increased discharge of contaminated groundwater to surface waters? |  |  |
| Provide citation to applicable study and summarize findings relative to the amount of infiltration that is permissible: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |
| Infiltration Screening Results (check box corresponding to result): |
| 8 | Is there substantial evidence that infiltration from the project would result in a significant increase in I&I to the sanitary sewer that cannot be sufficiently mitigated? (See Appendix XVII) Provide narrative discussion and supporting evidence: Summarize findings of studies provide reference to studies, calculations, maps, data sources, etc. Provide narrative discussion of study/data source applicability. |  |
| 9 | If any answer from row 1-3 is yes: infiltration of any volume is not feasible within the DMA or equivalent. Provide basis: Summarize findings of infeasibility screening |  |
| 10 | If any answer from row 4-7 is yes, infiltration is permissible but is not presumed to be feasible for the entire DCV. Criteria for designing biotreatment BMPs to achieve the maximum feasible infiltration and ET shall apply. Provide basis: Summarize findings of infeasibility screening |  |
| 11 | If all answers to rows 1 through 11 are no, infiltration of the full DCV is potentially feasible, BMPs must be designed to infiltrate the full DCV to the maximum extent practicable. |  |

| Worksheet A: Hydrologic Source Control Calculation Form |
| --- |
|  | Drainage area ID |  |  |  |
|  | Total drainage area |  | acres |  |
| Total drainage area Impervious Area (IAtotal) |  | acres |  |
| HSC ID | HSC Type/ Description/ Reference BMP Fact Sheet | Effect of individual HSCi per criteria in BMP Fact Sheets (XIV.1) (dHSCi)1 | Impervious Area Tributary to HSCi (IAi) | di × IAi |
|  | Box 1: | ∑ di × IAi = |  |
|  | Box 2: | IAtotal = |  |
|  | [Box 1]/[Box 2]: | dHSC total = |  |
|  |  | Percent Capture Provided by HSCs (Table III.1) |  |

1 - For HSCs meeting criteria to be considered self-retaining, enter the DCV for the project.

| Worksheet B: Simple Design Capture Volume Sizing Method |
| --- |
| Step 1: Determine the design capture storm depth used for calculating volume |
| 1 | Enter design capture storm depth from Figure III.1, d (inches) | d= |  | inches |
| 2 | Enter the effect of provided HSCs, dHSC (inches) (Worksheet A) | dHSC= |  | inches |
| 3 | Calculate the remainder of the design capture storm depth, dremainder (inches) (Line 1 – Line 2) | dremainder= |  | inches |
| Step 2: Calculate the DCV |
| 1 | Enter Project area tributary to BMP (s), A (acres) | A= |  | acres |
| 2 | Enter Project Imperviousness, imp (unitless) | imp= |  |  |
| 3 | Calculate runoff coefficient, C= (0.75 x imp) + 0.15 | C= |  |  |
| 4 | Calculate runoff volume, Vdesign= (C x dremainder x A x 43560 x (1/12)) | Vdesign= |  | cu-ft |
| Step 3: Design BMPs to ensure full retention of the DCV |
| Step 3a: Determine design infiltration rate |
| 1 | Enter measured infiltration rate, Kmeasured (in/hr) (Appendix VII) | Kmeasured= |  | In/hr |
| 2 | Enter combined safety factor from Worksheet H, Sfinal (unitless) | Sfinal= |  |  |
| 3 | Calculate design infiltration rate, Kdesign = Kmeasured / Sfinal | Kdesign= |  | In/hr |
| Step 3b: Determine minimum BMP footprint |
| 4 | Enter drawdown time, T (max 48 hours) | T= |  | Hours |
| 5 | Calculate max retention depth that can be drawn down within the drawdown time (feet), Dmax = Kdesign x T x (1/12) | Dmax= |  | feet |
| 6 | Calculate minimum area required for BMP (sq-ft), Amin = Vdesign/ dmax | Amin= |  | sq-ft |

| Worksheet C: Capture Efficiency Method for Volume-Based, Constant Drawdown BMPs |
| --- |
| Step 1: Determine the design capture storm depth used for calculating volume |
| 1 | Enter design capture storm depth from Figure III.1, d (inches) | d= |  | inches |
| 2 | Enter calculated drawdown time of the proposed BMP based on equation provided in applicable BMP Fact Sheet, T (hours) | T= |  | hours |
| 3 | Using Figure III.2, determine the "fraction of design capture storm depth" at which the BMP drawdown time (T) line achieves 80% capture efficiency, X1 | X1= |  |  |
| 4 | Enter the effect depth of provided HSCs upstream, dHSC (inches) (Worksheet A) | dHSC= |  | inches |
| 5 | Enter capture efficiency corresponding to dHSC, Y2 (Worksheet A) | Y2= |  | % |
| 6 | Using Figure III.2, determine the fraction of "design capture storm depth" at which the drawdown time (T) achieves the equivalent of the upstream capture efficiency(Y2), X2 | X2= |  |  |
| 7 | Calculate the fraction of design volume that must be provided by BMP, fraction = X1 - X2 | fraction= |  |  |
| 8 | Calculate the resultant design capture storm depth (inches), dfraction= fraction × d | dfraction= |  | inches |
| Step 2: Calculate the DCV |
| 1 | Enter Project area tributary to BMP (s), A (acres) | A= |  | acres |
| 2 | Enter Project Imperviousness, imp (unitless) | imp= |  |  |
| 3 | Calculate runoff coefficient, C= (0.75 x imp) + 0.15 | C= |  |  |
| 4 | Calculate runoff volume, Vdesign= (C x drfraction x A x 43560 x (1/12)) | Vdesign= |  | cu-ft |
| Supporting Calculations |
| Describe system: |
| Provide drawdown time calculations per applicable BMP Fact Sheet: |
| Graphical Operations |
| Provide supporting graphical operations. See Example III.6. |

| Worksheet D: Capture Efficiency Method for Flow-Based BMPs |
| --- |
| Step 1: Determine the design capture storm depth used for calculating volume |
| 1 | Enter the time of concentration, Tc (min) (See Appendix IV.2) | Tc= |  |  |
| 2 | Using Figure III.4, determine the design intensity at which the estimated time of concentration (Tc) achieves 80% capture efficiency, I1 | I1= |  | in/hr |
| 3 | Enter the effect depth of provided HSCs upstream, dHSC (inches) (Worksheet A) | dHSC= |  | inches |
| 4 | Enter capture efficiency corresponding to dHSC, Y2 (Worksheet A) | Y2= |  | % |
| 5 | Using Figure III.4, determine the design intensity at which the time of concentration (Tc) achieves the upstream capture efficiency(Y2), I2 | I2= |  |  |
| 6 | Determine the design intensity that must be provided by BMP, Idesign= I1-I2 | Idesign= |  |  |
| Step 2: Calculate the design flowrate |
| 1 | Enter Project area tributary to BMP (s), A (acres) | A= |  | acres |
| 2 | Enter Project Imperviousness, imp (unitless) | imp= |  |  |
| 3 | Calculate runoff coefficient, C= (0.75 x imp) + 0.15 | C= |  |  |
| 4 | Calculate design flowrate, Qdesign= (C x idesign x A) | Qdesign= |  | cfs |
| Supporting Calculations |
| Describe system: |
| Provide time of concentration assumptions: |
| Graphical Operations |
| Provide supporting graphical operations. See Example III.7. |

| Worksheet E: Determining Capture Efficiency of Volume Based, Constant Drawdown BMP based on Design Volume |
| --- |
| Step 1: Determine the design capture storm depth used for calculating volume |
| 1 | Enter design capture storm depth from Figure III.1, d (inches) | d= |  | inches |
| 2 | Enter the storage volume provided in the BMP, V (cu-ft) | V= |  | cu-ft |
| 3 | Enter Project area tributary to BMP (s), A (acres) | A= |  | acres |
| 4 | Enter Project Imperviousness, imp (unitless) | imp= |  |  |
| 5 | Calculate runoff coefficient, C= (0.75 x imp) + 0.15 | C= |  |  |
| 6 | Calculate the effective design storm depth provided (inches), dprovided=(V × 12)/(C × A × 43560) | dprovided= |  | inches |
| 7 | Calculate the design storm depth as a fraction of the design capture depth, Xfraction = dprovided/d | Xfraction= |  |  |
| Step 2: Calculate the capture efficiency of the BMP system |
| 1 | Determine the drawdown time of the proposed BMP based on equations provided in the applicable BMP Fact Sheet, T (hours) | T= |  | hours |
| 2 | Enter the effect of provided HSCs upstream, dHSC (inches) (Worksheet A) | dHSC= |  | inches |
| 3 | Enter capture efficiency corresponding to dHSC from Table 6.7 (regionally based), Y1 (Worksheet A) | Y1= |  | % |
| 4 | Using Figure III.2, determine the fraction of "design capture storm depth" at which the drawdown time (T) achieves the upstream capture efficiency(Y1), X1 | X1= |  |  |
| 5 | Determine the fraction of design capture storm depth corresponding to the cumulative capture efficiency, X2=X1+Xfraction | X2= |  |  |
| 6 | Using Figure III.2, determine the capture efficiency corresponding to total fraction of design storm depth (X2) for drawdown time (T), Y2 | Y2= |  | % |
| Supporting Calculations |
| Describe system: |
| Provide drawdown calculations per equations in applicable BMP Fact Sheet: |
| Graphical Operations |
| Use this graph to provide the supporting graphical operations. See Example III.8. |

| Worksheet F: Determining Capture Efficiency of a Flow-based BMP based on Treatment Capacity |
| --- |
| Step 1: Determine the design intensity used for calculating design flowrate |
| 1 | Determine the design flowrate of the BMP, Q (cfs) | Q= |  | cfs |
| 2 | Enter Project Imperviousness, imp (unitless) | imp= |  |  |
| 3 | Calculate runoff coefficient, C= (0.75 x imp) + 0.15 | C= |  |  |
| 4 | Back calculate the equivalent intensity of rainfall treated in the BMP (cfs), iprovided=Q/C | iprovided= |  | in/hr |
| Step 2: Calculate the capture efficiency of theflow-based BMP |
| 1 | Enter the time of concentration, Tc (min) (Section IV.2) | Tc= |  |  |
| 2 | Enter the effect of provided HSCs upstream, dHSC (inches) (Worksheet A) | dHSC= |  | inches |
| 3 | Enter the upstream capture efficiency corresponding to dHSC from Table III.1 (regionally based), Y1 (Worksheet A) | Y1= |  | % |
| 4 | Using Figure III.4, determine the design intensity at which the time of concentration (Tc) achieves the upstream capture efficiency(Y1), I1 | I1= |  | in/hr |
| 5 | Determine the cumulative design intensity that is provided by upstream and project BMPs, I2 = Iprovided + I1 | I2= |  | in/hr |
| 6 | Using Figure III.4, determine the capture efficiency corresponding to the total intensity captured (I2) for time of concentration (Tc) for upstream and Project BMPs, Y2 | Y2= |  | % |
| Supporting Calculations |
| Describe system: |
| Provide time of concentration assumptions: |
| Graphical Operations |
| Provide supporting graphical operations. |

| Worksheet G: Alternative Compliance Volume Worksheet |
| --- |
| Step 1: Determine the alternative compliance volume without water quality credits |
| 1 | Determine the capture efficiency achieved in upstream BMPs using Appendix III, X1 (%) | X1= |  | % |
| 2 | Enter design capture storm depth from Figure III.1, d (inches) | d= |  | inches |
| 3 | Using Figure VI.1, pivot from where X1 intersects the curve to determine the fraction of design capture storm depth remaining to be met, Y1 | Y1= |  |  |
| 4 | Calculate the design depth that must be managed in alternative compliance BMPs, dalternative = Y1 × d | dalternative= |  | inches |
| 5 | Compute the alternative compliance volume corresponding to dalternative using the hydrologic methods described in Section III.1.1, ACV (cu-ft) | ACV= |  | cu-ft |
| Step 2: Determine Credit Volume |
| Method 1: Determine Credit Volume based on Reducing Impervious Footprint |
| 1 | Enter design capture storm depth from Figure III.1, d (inches) | d= |  | inches |
| 2 | Using d, calculate the DCV using the pre-project imperviousness and the methods described in Appendix III, DCVpre (cu-ft). | DCVpre= |  | cu-ft |
| 3 | Using d, calculate the DCV using the proposed imperviousness and the methods described in Appendix III, DCVpost (cu-ft). | DCVpost= |  | cu-ft |
| 4 | Calculate the Credit Volume = DCVpre - DCVpost (cu-ft). | Credit Volume= |  | cu-ft |
| Method 2: Determine Credit Volume based on Project Type and Density |
| 1 | Determine the sum of the Credit Percentages applicable to the Project, ∑Credit Percentages (%). (See Section 3.1 of the Model WQMP) | ∑Credit Percentages = |  | % |
| 2 | Enter design capture storm depth from Figure III.1, d (inches) | d= |  | inches |
| 3 | Using d, calculate the DCV using the proposed imperviousness without BMPs and the methods described in Appendix III, DCVpost no BMP (cu-ft). | DCVpost no BMP= |  | cu-ft |
| 4 | Calculate the Credit Volume = DCVpost no BMP × ∑Credit Percentages | Credit Volume= |  | cu-ft |
| Step 3: Determine the Alternative Compliance Volume after WQ Credits |
| 1 | Enter design capture storm depth from Figure III.1, d (inches) | d= |  | inches |
| 2 | Using d, calculate the DCV using the proposed imperviousness and the methods described in Appendix III, DCVpost (cu-ft). | DCVpost= |  | cu-ft |
| 3 | Calculate the alternative compliance volume, ACV = DCVpost - Credit Volume | ACV= |  | cu-ft |

| Worksheet H: Factor of Safety and Design Infiltration Rate Worksheet |
| --- |
| Factor Category | Factor Description | Assigned Weight (w) | Factor Value (v) | Product (p) p = w x v |
| A | Suitability Assessment | Soil assessment methods | 0.25 |  |  |
|  |  | Predominant soil texture | 0.25 |  |  |
|  |  | Site soil variability | 0.25 |  |  |
|  |  | Depth to groundwater / impervious layer | 0.25 |  |  |
|  |  | Suitability Assessment Safety Factor, SA = (p |  |
| B | Design | Tributary area size | 0.25 |  |  |
|  |  | Level of pretreatment/ expected sediment loads | 0.25 |  |  |
|  |  | Redundancy | 0.25 |  |  |
|  |  | Compaction during construction | 0.25 |  |  |
|  |  | Design Safety Factor, SB = (p |  |
| Combined Safety Factor, STOT= SA x SB |  |
| Measured Infiltration Rate, inch/hr, KM (corrected for test-specific bias) |  |
| Design Infiltration Rate, in/hr, KDESIGN = STOT / KM |  |
| Supporting Data |
| Briefly describe infiltration test and provide reference to test forms: |

Note: The minimum combined adjustment factor shall not be less than 2.0 and the maximum combined adjustment factor shall not exceed 9.0.

| Worksheet I: Summary of Groundwater-related Feasibility Criteria |
| --- |
| 1 | Is project large or small? (as defined by Table VIII.2) circle one | Large Small |
| 2 | What is the tributary area to the BMP? | A |  | acres |
| 3 | What type of BMP is proposed? |  |
| 4 | What is the infiltrating surface area of the proposed BMP? | ABMP |  | sq-ft |
| 5 | What land use activities are present in the tributary area (list all) |
| 6 | What land use-based risk category is applicable? | L | M | H |
| 7 | If M or H, what pretreatment and source isolation BMPs have been considered and are proposed (describe all): |
| 8 | What minimum separation to mounded seasonally high groundwater applies to the proposed BMP? See Section VIII.2 (circle one) | 5 ft 10 ft |
| 9 | Provide rationale for selection of applicable minimum separation to seasonally high mounded groundwater: |
| 10 | What is separation from the infiltrating surface to seasonally high groundwater? | SHGWT |  | ft |
| 11 | What is separation from the infiltrating surface to mounded seasonally high groundwater? | Mounded SHGWT |  | ft |
| 12 | Describe assumptions and methods used for mounding analysis: |
| 13 | Is the site within a plume protection boundary (See Figure VIII.2)? | Y N N/A |
| 14 | Is the site within a selenium source area or other natural plume area (See Figure VIII.2)? | Y N N/A |
| 15 | Is the site within 250 feet of a contaminated site? | Y N N/A |
| 16 | If site-specific study has been prepared, provide citation and briefly summarize relevant findings: |
| 17 | Is the site within 100 feet of a water supply well, spring, septic system? | Y N N/A |
| 18 | Is infiltration feasible on the site relative to groundwater-related criteria? | Y N |
| Provide rationale for feasibility determination: |

Note: if a single criterion or group of criteria would render infiltration infeasible, it is not necessary to evaluate every question in this worksheet.

| Worksheet J: Summary of Harvested Water Demand and Feasibility |
| --- |
| 1 | What demands for harvested water exist in the tributary area (check all that apply): |
| 2 | Toilet and urinal flushing | □ |
| 3 | Landscape irrigation | □ |
| 4 | Other:_______________________________________________________ | □ |
| 5 | What is the design capture storm depth? (Figure III.1) | d |  | inches |
| 6 | What is the project size? | A |  | ac |
| 7 | What is the acreage of impervious area? | IA |  | ac |
|  | For projects with both toilet flushing and indoor demand |  |  |
| 8 | What is the minimum use required for partial capture? (Table X.6) |  | gpd |
| 9 | What is the project estimated minimum wet season total daily use? |  | gpd |
| 10 | Is partial capture potentially feasible? (Line 9 > Line 8?) |  |  |
|  | For projects with only toilet flushing demand |  |  |
| 11 | What is the minimum TUTIA for partial capture? (Table X.7) |  |  |
| 12 | What is the project estimated TUTIA? |  |  |
| 13 | Is partial capture potentially feasible? (Line 12 > Line 11?) |  |  |
|  | For projects with only irrigation demand |  |  |
| 14 | What is the minimum irrigation area required based on conservation landscape design? (Table X.8) |  | ac |
| 15 | What is the proposed project irrigated area? (multiply conservation landscaping by 1; multiply active turf by 2) |  | ac |
| 16 | Is partial capture potentially feasible? (Line 15 > Line 14?) |  |  |
| Provide supporting assumptions and citations for controlling demand calculation: |